## Slide 1: IP ADDRESSES

## Slide 2: What is an IP Address
An IP (Internet Protocol) address is a unique identifier assigned to each device connected to a network that uses the Internet Protocol for communication.
It serves two primary functions:
  Identifying the host or network interface
  Providing the location of the host in the network.
Two versions of an IP Addresses
  IPV4 – 4,294,967296 (Total no. of addresses)
  IPV6
IPv4:Format: xxx.xxx.xxx.xxx, where each xxx can range from 0 to 255.Example: 192.168.1.1
IPv6 Format: 2001:0db8:85a3:0000:0000:8a2e:0370:7334

## Slide 3: Management of an IP Addresses
The management and assignment of IP addresses are handled by a hierarchical system of organizations that operate at different levels, from global to local. Here's how IP address management works:
Internet Assigned Numbers Authority (IANA)
  Role:
    IANA is a department of the Internet Corporation for Assigned Names and Numbers (ICANN), which is responsible for coordinating global IP address allocation, as well as the management of the DNS root zone, and other critical aspects of the internet's infrastructure.
  Responsibilities:
    Allocates large blocks of IP addresses to Regional Internet Registries (RIRs).
    Manages IP address space for both IPv4 and IPv6.
    Oversees the distribution of other internet numbers, such as Autonomous System Numbers (ASNs).

## Slide 4: Management of an IP Addresses
Regional Internet Registries (RIRs)
Role:
    RIRs are organizations that manage the allocation and registration of IP addresses within specific regions of the world. There are five RIRs, each serving a different region.
Responsibilities:
    Receive large blocks of IP addresses from IANA and allocate smaller blocks to ISPs, data centers, and other organizations within their region.
    Maintain databases of IP address allocations and registrations, ensuring that IP address assignments are properly documented.
    Provide services like WHOIS, which allows the public to look up who owns a particular IP address.

## Slide 5: Management of an IP Addresses
The Five RIRs
ARIN (American Registry for Internet Numbers): Covers the United States, Canada, and parts of the Caribbean.
RIPE NCC (Réseaux IP Européens Network Coordination Centre): Covers Europe, the Middle East, and parts of Central Asia.
APNIC (Asia-Pacific Network Information Centre): Covers Asia and the Pacific region.
LACNIC (Latin American and Caribbean Internet Addresses Registry): Covers Latin America and parts of the Caribbean.
AFRINIC (African Network Information Centre): Covers Africa and parts of the Indian Ocean region.

## Slide 6: Management of an IP Addresses
Internet Service Providers (ISPs)
Role:
ISPs are companies that provide internet access to end-users (both individuals and businesses). They are assigned blocks of IP addresses by the RIRs.
Responsibilities:
  Allocate IP addresses to their customers, either dynamically (changing with each connection) or statically (fixed for a particular customer).
  Manage the routing of IP traffic for their customers using the IP addresses they've been assigned.
  Sometimes further subdivide their IP address blocks and assign smaller subnets to organizations or large customers.

## Slide 7: Management of an IP Addresses
End-User Organizations
Role:
These are businesses, institutions, or individuals who receive IP address assignments from their ISPs or directly from the RIRs if they require large blocks of IP addresses (e.g., large enterprises, data centers).
Responsibilities:
  Use the assigned IP addresses to manage their internal networks.
  Configure their network devices (e.g., routers, servers) to use the assigned IP addresses.
  Ensure proper security and management of the IP addresses within their network.

## Slide 8: IP Address Classes
Reason for Dividing IP Addresses into Classes
Simplification of Address Allocation Purpose:
  By categorizing IP addresses into different classes (A, B, C, D, and E), the system allowed for the easy allocation of IP addresses based on the size of the network.
  Different classes were designed to accommodate networks of varying sizes, from very large networks to small ones.
Outcome: This made the process of assigning IP addresses more straightforward for network administrators and allowed for consistent and easy-to-understand routing protocols.

## Slide 9: IP Address Classes (Cont.)
Optimized IP Address Utilization:
  Different classes of IP addresses were created to ensure that IP address space could be efficiently used.
    Class A, with fewer networks but more hosts per network, was meant for very large organizations.
    Class B, with a moderate number of networks and hosts, was meant for medium-sized organizations.
    Class C, with many networks but fewer hosts per network, was meant for smaller organizations.
Outcome: This made the process of assigning IP addresses more straightforward for network administrators and allowed for consistent and easy-to-understand routing protocols.

## Slide 10: IP Address Classes (Cont.)
Simplification of Routing:
  Purpose: The class system made routing simpler because routers could easily determine the network part of an IP address by looking at its class. This made routing decisions faster and more efficient.
  Outcome: By knowing the class of an IP address, routers could quickly identify the network portion of the address and route packets to the correct network without needing complex calculations.
Support for Different Types of Communication
  Purpose: The classes also supported different types of communication:
    Class D addresses were reserved for multicast, which is used to send data to a group of destinations.
    Class E addresses were reserved for experimental use, ensuring that there was room for growth and new technologies.
Outcome: This categorization allowed the internet to support different types of data transmission, like broadcasting to multiple recipients, which is important for applications like streaming and conferencing.

## Slide 11: Classes of an IPV4 Address
Class A:
  First Octet Range: 1.0.0.0 to 126.0.0.0
  Default Subnet Mask: 255.0.0.0
  Network ID Bits: 8 bits
  Host ID Bits: 24 bits
  Total Networks: 2^7 = 128 (but only 126 are usable because 0.0.0.0 and 127.0.0.0 are reserved)
  Total Hosts per Network: 2^24 - 2 = 16,777,214
  Use Case: Large networks with many devices (e.g., large organizations).

## Slide 12: Classes of an IPV4 Address
Class B:
  First Octet Range: 128.0.0.0 to 191.255.0.0
  Default Subnet Mask: 255.255.0.0
  Network ID Bits: 16 bits
  Host ID Bits: 16 bits
  Total Networks: 2^14 = 16,384Total Hosts per Network: 2^16 - 2 = 65,534
  Use Case: Medium-sized networks (e.g., universities, enterprises).

## Slide 13: Classes of an IPV4 Address
Class C:
  First Octet Range: 192.0.0.0 to 223.255.255.0
  Default Subnet Mask: 255.255.255.0
  Network ID Bits: 24 bits
  Host ID Bits: 8 bits
  Total Networks: 2^21 = 2,097,152Total Hosts per Network: 2^8 - 2 = 254
  Use Case: Small networks (e.g., small businesses, home networks).

## Slide 14: Classes of an IPV4 Address
Class D:
  First Octet Range: 224.0.0.0 to 239.255.255.255
  Use Case: Used for multicasting; IP addresses in this range are not assigned to individual devices but to groups of devices.
Class E:
  First Octet Range: 240.0.0.0 to 255.255.255.255
  Use Case: Reserved for experimental purposes and is not used in general networking.

## Slide 15: What is Subnet Mask
  A subnet mask is a 32-bit number used in IP networks to divide an IP address into two parts:
    the network ID and the host ID.
  The subnet mask helps determine which portion of the IP address identifies the network and which portion identifies the specific device (host) within that network.
  Routers use the subnet mask to route traffic to the correct network
  Like an IP address, a subnet mask is also written in the dotted-decimal format, e.g., 255.255.255.0.
  The subnet mask has a series of consecutive 1 bits followed by a series of 0 bits.
  The 1 bits represent the network portion of the IP address.
  The 0 bits represent the host portion.

## Slide 16: Network ID Vs Host ID
Network ID (Network Portion):
  Definition: The network ID is the portion of an IP address that identifies a specific network within a larger network (like the internet). It is derived by applying the subnet mask to the IP address.
  How it Works: When an IP address is logically ANDed with a subnet mask, the result is the network ID. For example, if the IP address is 192.168.1.10 and the subnet mask is 255.255.255.0, the network ID would be 192.168.1.0.
  Purpose: The network ID is used by routers to determine the path that data should take to reach the correct destination network.

## Slide 17: Network ID Vs Host ID
Host ID (Host Portion):
  Definition: The host ID is the part of the IP address that identifies a specific device (or host) on the network.
  How it Works: The host ID is determined by the bits of the IP address that are not covered by the subnet mask. Continuing with the previous example, 192.168.1.10 in the network 192.168.1.0 has a host ID of 10.
  Purpose: The host ID is unique within its network and is used to route data to the correct device within that network.

## Slide 18: Private & Public IP Addresses
Public IP Address:
  Assigned by the Internet Assigned Numbers Authority (IANA) and are unique across the entire internet. These are used for communication over the internet.
Private IP Address:
  Reserved for use within private networks and are not routable on the internet. These include:
    Class A: 10.0.0.0 to 10.255.255.255
    Class B: 172.16.0.0 to 172.31.255.255
    Class C: 192.168.0.0 to 192.168.255.255
Special IP Addresses
  Loopback Address: 127.0.0.1 is used for testing purposes within a host.
  Broadcast Address: Sends data to all hosts on a network. E.g., 192.168.1.255 for a Class C network.

## Slide 19: Class full Vs Classless Addresses
Aspect | Class Full | Classless
Address Structure | Divides addresses into fixed classes (A, B, C, D, E). | No fixed classes; network and host portions are defined by a variable-length subnet mask.
Network Boundary | Fixed based on address class (e.g., /8, /16, /24). | Variable, based on subnet mask (e.g., /12, /28, etc.).
Routing Protocols | Uses classful routing protocols (e.g., RIP v1). | Uses classless routing protocols (e.g., OSPF, RIP v2).
IP Address Efficiency | Less efficient; can lead to wasted IP addresses. | More efficient; allows precise allocation of address space.
Flexibility | Limited; constrained by class boundaries. | Highly flexible; supports VLSM and more efficient subnetting.
CIDR Notation | Not applicable. | Uses CIDR notation (e.g., 192.168.1.0/24).

## Slide 20: Subnetting
  Subnetting is the process of dividing a larger network into smaller, more manageable sub-networks (subnets).
  This is done by adjusting the subnet mask to create more network bits, reducing the number of bits available for hosts.
  For instance, if you have a Class C network (192.168.1.0/24), you can create subnets by extending the subnet mask beyond the default 255.255.255.0.
  A subnet mask of 255.255.255.128 would split the network into two subnets:192.168.1.0/25 (Hosts: 1-126)192.168.1.128/25 (Hosts: 129-254)

## Slide 21: Why Subnetting??
Efficient IP Address Management
  Avoiding Waste: Without subnetting, a single network might have more IP addresses than needed, leading to wastage. For example, a Class A network (10.0.0.0/8) has over 16 million IP addresses, far more than most organizations need. Subnetting allows the network to be divided into smaller subnets, each with a more appropriate number of IP addresses.
  Better Utilization: Subnetting enables the precise allocation of IP addresses to different departments or locations within an organization, ensuring that no IP addresses are left unused.
Improved Network Performance
  Reduced Broadcast Traffic: In a network, broadcast traffic is sent to all devices within that network. As the network grows, so does the broadcast traffic, which can slow down the entire network. Subnetting reduces the size of each network segment, thus limiting broadcast traffic to smaller areas and improving overall network performance.
  Optimized Routing: Smaller subnets mean that routers can more efficiently manage and route traffic. When a router receives a packet, it can quickly determine the destination subnet and route the packet accordingly, reducing latency and improving network speed.

## Slide 22: Why Subnetting??
Simplified Network Management
  Logical Grouping: Subnetting helps organize the network logically, grouping devices based on departments, functions, or locations. This logical structure simplifies network management, troubleshooting, and maintenance.
  Scalability: As an organization grows, subnetting allows for easier network expansion. New subnets can be added without disrupting the existing network, providing a flexible and scalable network infrastructure.
Reduced Network Congestion
  Smaller Collision Domains: In networks using technologies like Ethernet, subnetting reduces the size of collision domains (areas where packet collisions can occur). Smaller collision domains lead to fewer collisions, reducing network congestion and improving data transmission efficiency.